## Slide 1: A Parametric Dataset Generator For Updating Digital Twins Through 2D LiDAR Perceptual Data
26th of September 2024
Pim van den Akker
Mechanical Engineering, Control Systems Technology Supervisors: Elena Torta, Gijs van Rhijn
Committee: Elena Torta, dr.,Jos Elfring, dr. ir., Pieter Pauwels, dr. ir

## Slide 2
How can we provide additional information?
    2D LiDAR
Problem Statement
?
?
?
?
?
?

## Slide 3: Building Information Model (BIM)
  3D model made during building construction
  Semantic (labelled) information
  Readily available
  Convert BIM to 2D map with labels
  From BIM Initialize Digital Twin
  Digital twin: an up-to-date representation of real world
  Useful for robot navigation and object tracking
How do we keep the digital twin up to date?
    BIM Model
Problem Statement
  Chair
  Wall
  Pillar
  Door

## Slide 4: Updating Digital Twin
    Prior Map (Digital Twin)
    Real-World LiDAR data
    Combined
Problem Statement

## Slide 5: Digital Twin Mismatches
    Removed Chair
    New Chair
    Correct Chair
Problem Statement
How do we get the data to train the model?
  Digital Twin
  Real World
How to detect these mismatches automatically?
How to maintain semantics?
Our solution:
Train a computer vision model to detect the patterns
Train by giving examples

## Slide 6: Data Generation
Manually labelling real data
Computer generated (synthetic) data
Domain gap: Difference between synthetic and real world
  Resources: capturing, labelling
  Not much variety
  A lot of time
  Cheap, just compute time
  A lot of data
  As varied as your generator
  Perfect annotation
Problem statement

## Slide 7: Goals
Implement a computer vision model to detect mismatches
A parametric dataset generator that emulates the data representing a building’s digital twin and LiDAR
Making specific datasets for specific environments
Problem Statement

## Slide 8: Parametric Dataset Generator
User defined data generation parameters
User controls the object dimensions
Specific objects for specific environments
Variety in data!
    For machine learning robustness
    Reduce domain gap
How do we generate varied environments?
Methods

## Slide 9
How do we simulate the “real world”?
Methods
Notes: Random examples separate video

## Slide 10: 2D LiDAR Simulation
Simulation:
    Generated environment
    Noise
Noise types:
Sensor noise
Localization and sensor artifact noise
How do we use this to simulate mismatches?
Methods

## Slide 11: Generating The Mismatches
Methods
    Starting Point
    Add object with only LiDAR: New Object
    Remove Digital Twin information: Removed Object
Classes: Correct Chair, Removed Chair, New Chair – Correct Pillar, Removed Pillar, New Pillar - Door

## Slide 12: Computer Vision Model
    Input image
Chair, Removed: 1
Pillar, Correct 1
Pillar, New 1
Output/ground truth
Bounding boxes
Labels
Mask shape
Chair, Removed 2
    Instance segmentation model: Mask R-CNN
Methods
Notes: Add colors to each type of output and match it with the image

## Slide 13: Generated Training Data
Input
Ground truth
Does this represent the real world?
…
…
    n = 1
    n = 2
    n = 3
    n = 4000
Methods

## Slide 14: Real-World Test Dataset
120 hand labelled examples
Data not used in training
How does the model perform on the test set?
Methods

## Slide 15: Qualitative Model Performance On Real World
    Input Image
    Bounding Box Ground Truth
    Bounding Box Model Prediction
    Mask Ground Truth
    Mask Model Prediction
15
Methods
It trains!
    Shape completion!
Notes: It trains!

## Slide 16: Qualitative Model Performance On Real World
16
    Input Image
    Bounding Box Model Prediction
    Bounding Box Ground Truth
    Mask Model Prediction
    Mask Ground Truth
Results

## Slide 17: Overconfident predictions
  Chair
  LiDAR
Two overlapping wrong predictions
Inherent to the model
How do we mitigate this issue?
Find the area of overlap
Treat these areas as not dependable
Is this information useless?
No, make overlapping prediction a hypothesis
Hypothesis is correct if a predicted label corresponds to ground truth
Almost time for experiments!
Results

## Slide 18: Metrics
IoU =
Results
Metric | 
mean Average Precision (mAP) | Measures detection across multiple thresholds.
True Positive Rate (TPR): | Proportion of positive instances correctly classified by the model.
Hypothesis TPR | TPR for hypothesis
Mask Intersection over Union (IoU) | Measuring mask accuracy

## Slide 19: Experiment 1
Goal:
How does performance compare to the real-world vs synthetic data?
Methodology:
Test on the real world and synthetic dataset
Results
Notes: Overview slide tussen de verschillende experiment slides

## Slide 20: Experiment 1: Bounding box mAP
Results
Chart: Categories
| Combined Class | Pillar Correct | Pillars Removed | Pillars New | Doors | Chair Correct | Chairs Removed | Chairs New
Real world data | 0.73572 | 0.84683 | 0.85085 | 0.57823 | 0.48067 | 0.94012 | 0.88653 | 0.73543
Synthetic data | 0.81192 | 0.96806 | 0.99428 | 0.6547 | 0.87219 | 0.75096 | 0.91826 | 0.47213
Mean average precision (mAP)
    Domain gap
    Input Image
    Model Prediction

## Slide 21: Experiment 1 Results
There exists a “domain gap”
Mask IoU works better on real world data
Real World dataset easier than synthetic in some cases
Metric | True Positive Rate | Mask Intersection over Union | Hypothesis True Positive Rate
Real World Data | 0.80 | 0.86 | 0.93
Synthetic Data | 0.85 | 0.78 | 0.97
Chart: Class
| Combined Class | Pillar Correct | Pillars Removed | Pillars New | Doors | Chair Correct | Chairs Removed | Chairs New
Real world data | 0.73572 | 0.84683 | 0.85085 | 0.57823 | 0.48067 | 0.94012 | 0.88653 | 0.73543
Synthetic data | 0.79192 | 0.96806 | 0.99428 | 0.6547 | 0.87219 | 0.75096 | 0.91826 | 0.47213
Mean average precision (mAP)
Results

## Slide 22: Experiment 2
Goal:
Does making a customized dataset for a specific environment help?
Methodology:
Create and train on customized vs generalized dataset
Results
Notes: Overview slide tussen de verschillende experiment slides

## Slide 23: Experiment 2 Results Bounding box mAP
Chart: Class
| Combined | Pillar Correct | Pillars Removed | Pillars New | Doors | Chair Correct | Chairs Removed | Chairs New
Customized | 0.79187 | 0.96806 | 0.99428 | 0.65469 | 0.87219 | 0.75094 | 0.91826 | 0.47183
General | 0.76154 | 0.94594 | 0.98759 | 0.55736 | 0.85095 | 0.73279 | 0.90679 | 0.44428
Results

## Slide 24: Discussion
Too little information for classification for new objects
Domain gap exists
More real-world test data is needed
Discussion & Conclusion

## Slide 25: Conclusion
An open-source dataset generator for creating examples of mismatches
Trained a model exclusively on synthetic data
A promising model for updating digital twins from 2D LiDAR data while maintaining semantics!
Future work
More object types
More and varied real world test data
Close the loop
Discussion & Conclusion

## Slide 26: Appendix

## Slide 27: Overconfident predictions
You untrustworthy little model?
  Chair
  LiDAR

## Slide 28: Detecting areas of overlap
Find areas with overlap (hypothesis area)
Quantify the amount of overlap
Threshold the overlap
These areas are called hypothesis areas
Hypothesis is correct if a predicted label corresponds to ground truth
Time for experiments!
Overlap Threshold
Intersection
Union
=
<
Hypothesis area

## Slide 29: Qualitative Model Performance on real world
Input Image
Bounding Box Ground Truth
Bounding Box Prediction
Masks Truth Ground
Masks prediction
Notes: It trains!

## Slide 30: Experiments
Experiment 3 goal:
Gain insight into data generation parameters
Experiment 3 Methodology:
Ablation experiments
Notes: Overview slide tussen de verschillende experiment slides

## Slide 31: Experiment 3 ResultsmAP Combined Ablation results Bounding Boxes
Chart: 
| LiDAR High Freq. | LiDAR Low Freq | LiDAR Block Size | Pillar Width | Chair Size | Pillar Chair Block Size
Ablation Parameters | 0.71896 | 0.73362 | 0.71729 | 0.70613 | 0.72278 | 0.60448

## Slide 32: Mask R-CNN